## Slide 1: Chapter 6 Architecture (2)
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Goals
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lights, Camera, Action: Compiling, Assembling, & Loading
Odds and Ends

## Slide 3: Programming
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Common high-level software constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 4: Arithmetic/logic Instructions
Logic instructions
and, or, xor, nor
  and: useful for masking bits
    Masking all but the least significant byte of a value:
    0xF234012F AND 0x000000FF = 0x0000002F
  or: useful for combining bit fields
    Combine 0xF2340000 with 0x000012BC:
    0xF2340000 OR 0x000012BC = 0xF23412BC
  nor: useful for inverting bits:
    A NOR $0 = NOT A
andi, ori, xori
  16-bit immediate is zero-extended (not sign-extended)
  nori not needed

## Slide 5: Arithmetic/logic Instructions
Logic instructions
Example 1

## Slide 6: Arithmetic/logic Instructions
Logic instructions
Example 1

## Slide 7: Arithmetic/logic Instructions
Logic instructions
Example 2

## Slide 8: Arithmetic/logic Instructions
Logic instructions
Example 2

## Slide 9: Arithmetic/logic Instructions
Shift instructions
sll: shift left logical
  Example: sll $t0, $t1, 5 # $t0 <= $t1 << 5
srl: shift right logical
  Example: srl $t0, $t1, 5 # $t0 <= $t1 >>> 5
sra: shift right arithmetic
  Example: sra $t0, $t1, 5 # $t0 <= $t1 >> 5

## Slide 10: Arithmetic/logic Instructions
Variable Shift instructions
sllv: shift left logical variable
  Example: sllv $t0, $t1, $t2 # $t0 <= $t1 << $t2
srlv: shift right logical variable
  Example: srlv $t0, $t1, $t2 # $t0 <= $t1 >>> $t2
srav: shift right arithmetic variable
  Example: srav $t0, $t1, $t2 # $t0 <= $t1 >> $t2

## Slide 11: Arithmetic/logic Instructions
Shift instructions

## Slide 12: Arithmetic/logic Instructions
Generating Constants
16-bit constants using addi:
32-bit constants using load upper immediate (lui) and ori:
C Code
int a = 0xFEDC8765;
MIPS assembly code
# $s0 = a
lui $s0, 0xFEDC
ori $s0, $s0, 0x8765
C Code
// int is a 32-bit signed word
int a = 0x4f3c;
MIPS assembly code
# $s0 = a
addi $s0, $0, 0x4f3c

## Slide 13: Arithmetic/logic Instructions
Multiplication and Division
Special registers: lo, hi
32 × 32 multiplication, 64 bit result
  mult $s0, $s1
  Result in {hi, lo}
32-bit division, 32-bit quotient, remainder
  div $s0, $s1
  Quotient in lo
  Remainder in hi
Moves from lo/hi special registers
  mflo $s2 #load the upper 32 bits from the product register
  mfhi $s3 #load the lower 32 bits from the product register

## Slide 14: Review: Stored Program

## Slide 15: Branching
Execute instructions out of sequence
Types of branches:
  Conditional
  branch if equal (beq)
  branch if not equal (bne)
  Unconditional
  jump (j)
  jump register (jr)
  jump and link (jal)
Notes: Other conditional instructions: bge, bgt bgtz, bgez, ble, blt, blez, bltz

## Slide 16: Branching
Conditional Branching: beq
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
beq $s0, $s1, target # branch is taken
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target: # label
add $s1, $s1, $s0 # $s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)

## Slide 17: Branching
Conditional Branching: bne
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
bne $s0, $s1, target # branch not taken
addi $s1, $s1, 1 # $s1 = 4 + 1 = 5
sub $s1, $s1, $s0 # $s1 = 5 – 4 = 1
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5
Notes: Other instructions: bge, bgt bgtz, bgez, ble, blt, blez, bltz

## Slide 18: Branching
Other MIPS branch instructions
beq, bne, bgtz, bltz, bgez, blez
- the only conditional branch opcodes
slt - set on less then
- for >, <, >=, <= comparisons between two registers
- slt rd, rs, rt # if rs < rt, rd = 1;
else rd = 0;
Notes: Other instructions: bge, bgt bgtz, bgez, ble, blt, blez, bltz

## Slide 19: Branching
Unconditional Branching: j
# MIPS assembly
addi $s0, $0, 4 # $s0 = 4
addi $s1, $0, 1 # $s1 = 1
j target # jump to target
sra $s1, $s1, 2 # not executed
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5

## Slide 20: Branching
Unconditional Branching: jr
# MIPS assembly
0x00002000 addi $s0, $0, 0x2010
0x00002004 jr $s0
0x00002008 addi $s1, $0, 1
0x0000200C sra $s1, $s1, 2
0x00002010 lw $s3, 44($s1)
jr is an R-type instruction.

## Slide 21: High Level Code Constructs
if statements
if/else statements
while loops
for loops

## Slide 22: High Level Code Constructs
if statements
if/else statements
while loops
for loops
C Code
if (i == j)
f = g + h;
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
L1: sub $s0, $s0, $s3
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 23: High Level Code Constructs
if statements
if/else statements
while loops
for loops
C Code
if (i == j)
f = g + h;
else
f = f – i;
MIPS assembly code
# $s0 = f, $s1 = g, $s2 = h
# $s3 = i, $s4 = j
bne $s3, $s4, L1
add $s0, $s1, $s2
j done
L1: sub $s0, $s0, $s3
done:

## Slide 24: High Level Code Constructs
if statements
if/else statements
while loops
for loops
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
MIPS assembly code
# $s0 = pow, $s1 = x
addi $s0, $0, 1
add $s1, $0, 0
addi $t0, $0, 128
while: beq $s0, $t0, done
sll $s0, $s0, 1
addi $s1, $s1, 1
j while
done:

## Slide 25: High Level Code Constructs
if statements
if/else statements
while loops
for loops
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
add $s0, $0, $0
addi $t0, $0, 10
for: beq $s0, $t0, done
add $s1, $s1, $s0
addi $s0, $s0, 1
j for
done:

## Slide 26: High Level Code Constructs
if statements
if/else statements
while loops
for loops – less than comparison
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
MIPS assembly code
# $s0 = i, $s1 = sum
addi $s1, $0, 0
addi $s0, $0, 1
addi $t0, $0, 101
loop: slt $t1, $s0, $t0
beq $t1, $0, done
add $s1, $s1, $s0
sll $s0, $s0, 1
j loop
done:
Notes: slt: set less than instruction:
rd=1 if rs < rd
rd=0 otherwise