## Slide 1: Chapter 1 From Zero to One (part 1)
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Goals
Background
Managing Complexity
The Digital Abstraction
Von Neumann Architecture
Number Systems
Logic Gates (Combinational & Sequential Logic )
Logic Levels
CMOS Transistors
Power Consumption

## Slide 3: Goals:
  Understand what’s under the hood of a computer
  Learn the principles of digital design
  Learn to systematically debug increasingly complex designs
  Design and build a microprocessor

## Slide 4: Background
Microprocessors have revolutionized our world
  Cell phones, Internet, rapid advances in medicine, etc.
The semiconductor industry has grown from $21 billion in 1985 to $300 billion in 2011

## Slide 5: Managing Complexity
  Abstraction
    Hiding details when they aren’t important.
  Discipline
    Act of intentionally restrict design choices
    More productive
    Example: digital discipline
  The Three –Y’s
  Hierarchy
    A system divided into modules and submodules
  Modularity
    Having well-defined functions and interfaces
  Regularity
    Encouraging uniformity, so modules can be easily reused

## Slide 6: Von Neumann Architecture
  Stored Program
  Instructions and data are logically the same and both stored in the same space (memory)
  Components
    CPU (Central Processing Unit)
      Arithmetic/Logic Unit (ALU)
      Control Unit (CU)
      Registers
        Program Counter (PC),
        Instruction Register (IR)
        Others: AC,MAR, MDR …
    Memory
    Input/Output devices

## Slide 7: Von Neumann Architecture
Von Neumann Architecture
  Level of abstraction for an electronic computing system

## Slide 8: Von Neumann Architecture
Central Processing Unit (CPU)
The CPU is the electronic circuit responsible for executing the instructions of a computer program.
The CPU contains the ALU, CU and a variety of registers
  Arithmetic/Logic Unit (ALU):
  Arithmetic operations (add, subtract etc.) and logic operations (AND, OR, NOT etc.) operations are carried out
  Control Unit (CU)
  Controls the operation of the computer’s ALU, memory and input/output devices. Provides the timing and control signals required by other computer components
  Registers
  High speed storage areas in the CPU. All data must be stored in register before it can be processed

## Slide 9: Von Neumann Architecture
  Registers
MAR | Memory Address Register | Holds the memory location of data that needs to be accessed
MDR | Memory Data Register | Holds data that is being transferred to or from memory
AC | Accumulator | Where intermediate arithmetic and logic results are stored
PC | Program Counter | Contains the address of the next instruction to be executed
CIR(IR) | Current Instruction Register | Contains the current instruction during processing

## Slide 10: Von Neumann Architecture
Buses
Buses are the means by which data is transmitted from one part of a computer to another, connecting all major internal components to the CPU and memory.
A standard CPU system bus is comprised of a control bus, data bus, and address bus
Address Bus | Carries the addresses of data (but not the data) between the processor and memory
Data Bus | Carries data between the processor, the memory unit and the input/output devices
Control Bus | Carries control signals/commands from the CPU (and status signals from other devices) in order to control and coordinate all the activities within the computer

## Slide 11: Von Neumann Architecture
Memory Unit
The memory unit consists of RAM, sometimes referred to as primary or main memory. Unlike a hard drive (secondary memory), this memory is fast and also directly accessible by the CPU.
RAM is split into partitions. Each partition consists of an address and its contents (both in binary form).
The address will uniquely identify every location in the memory.
Loading data from permanent memory (hard drive), into the faster and directly accessible temporary memory (RAM), allows the CPU to operate much quicker

## Slide 12: Von Neumann Architecture
  Fetch-Execute Cycle
The fetch-execute cycle is the basic operation (instruction) cycle of a computer.
During the fetch execute cycle, the computer retrieves a program instruction from its memory. It then establishes and carries out the actions that are required for that instruction.
The cycle of fetching, decoding, and executing an instruction is continually repeated by the CPU whilst the computer is turned on.

## Slide 13: Fetch-Execute Cycle

## Slide 14: Fetch-Execute Cycle
Stage | Description of Stage | Simplified Description
1 | The PC contains the address of the memory location that has the next instruction which has to be fetched | PC has address of next instruction
2 | This address is then copied from the PC to the MAR via the address bus | PC contents is copied to the MAR
3 | The contents (instruction) at the memory location (address) contained in MAR are then copied into the MDR | Lookup MAR and get contents. Copy contents into the MDR
4 | The contents (instruction) in the MDR is then copied and placed into the CIR | Copy MDR contents into the CIR
5 | The value in the PC is then incremented by 1 so that it now points to the next instruction which has to be fetched | PC is then incremented by 1
6 | The instruction is finally decoded and then executed by sending out signals (via control bus) to the various components of the computer | The instruction is decoded and then executed
7 | Repeat | 

## Slide 15: Number Systems
Number System
  Base and Symbols
  Positional notation and Weight
Data Representation

## Slide 16: Number Systems
Number System
  Base and Symbols
  Positional notation and Weight
Decimal
  Base 10, Symbols (0, 1, 2, 3, 4, 5, 6, 7, 8, 9)
Binary
  Base 2, Symbols (0, 1)
Hexadecimal
  Base 16, Symbols (0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E,F)
Octal decimal
  Base 8, Symbols (0, 1, 2, 3, 4, 5, 6, 7)

## Slide 17: Number Systems
Number System
  Base and Symbols
  Positional notation and Weight
642 in base 10 positional notation is:
6 x 102 = 6 x 100 = 600
+ 4 x 101 = 4 x 10 = 40
+ 2 x 10º = 2 x 1 = 2 = 642 in base 10
This number is in
base 10
The power indicates
the position of
the number

## Slide 18: Number Systems
Number System
  Base and Symbols
  Positional notation and Weight
dn-1 * Rn-1 + dn-2 * Rn-2 + ... + d1 * R1 + d0 * R0
General Formula:
642 is 6 * 102 + 4 * 10 + 2 * 1
R is the base
of the number
n is the number of
digits in the number
d is the digit in the
ith position
in the number

## Slide 19: Number Systems
Number System
  Base and Symbols
  Positional notation and Weight
What if 642 has the base of 13?
642 in base 13 is equivalent to 1068 in base 10
+ 6 x 132 = 6 x 169 = 1014
+ 4 x 131 = 4 x 13 = 52
+ 2 x 13º = 2 x 1 = 2
= 1068 in base 10

## Slide 20: Number Systems
Values and Range
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:

## Slide 21: Number Systems
Values and Range
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]

## Slide 22: Number Conversion
Binary to Decimal conversion
  Convert 100112 to decimal
Decimal to Binary conversion:
  Convert 4710 to binary

## Slide 23: Number Conversion
Binary to Decimal conversion
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to Binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112

## Slide 24: Number Conversion
Hexadecimal to Binary conversion
  Convert 4AF16 (also written 0x4AF) to binary
Hexadecimal to Decimal conversion:
  Convert 0x4AF to decimal

## Slide 25: Number Conversion
Hexadecimal to Binary conversion
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to Decimal conversion:
  Convert 0x4AF to decimal
  4×162 + 10×161 + 15×160 = 119910

## Slide 26: Review: Bits, Bytes, Nibbles
Bits
Bytes & Nibbles
Bytes
Notes: MSB: most significant bit/byte
LSB: least significant bit/byte

## Slide 27: Review: Power of Two
20 =
21 =
22 =
23 =
24 =
25 =
26 =
27 =
28 =
29 =
210 =
211 =
212 =
213 =
214 =
215 =
216 =
Notes: Exercise

## Slide 28: Review: Power of Two
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
216 = 65536
Notes: Exercise

## Slide 29: Review: Large Powers of Two
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
240 = 1 tera ≈ ?
250 = …
…
Notes: MSB: most significant bit/byte
LSB: least significant bit/byte

## Slide 30: Review: Large Powers of Two
Notes: MSB: most significant bit/byte
LSB: least significant bit/byte

## Slide 31: Exercise: estimate powers of two
What is the value of 224?
How many values can a 32-bit variable represent?
Notes: MSB: most significant bit/byte
LSB: least significant bit/byte

## Slide 32: Exercise: estimate powers of two
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Notes: Exercise

## Slide 33: Addition
Decimal addition
Binary addition
Hexadecimal
1 1 carries
12A6
+ 07CD
1A93
Notes: Exercise

## Slide 34: Exercise: Addition
Add the following 4-bit binary numbers:
1001 1011
+ 0101 + 0110
Add the following 4-bit hexadecimal numbers:
10A6 906A
+ 07CD + 70DC
Notes: Exercise

## Slide 35: Overflow
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
How to handle overflow ?
Notes: Exercise

## Slide 36: Signed Binary Numbers
Sign/Magnitude Numbers
Two’s Complement Numbers
Notes: Exercise

## Slide 37: Signed Binary Numbers
Sign/Magnitude Numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Q: 4-bit sign/magnitude representations of ± 6:
+6 = ?
- 6 = ?
Q: Range of an N-bit sign/magnitude number:
?
Notes: Exercise

## Slide 38: Signed Binary Numbers
Sign/Magnitude Numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Q: 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Q: Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Notes: Exercise

## Slide 39: Signed Binary Numbers
Sign/Magnitude Numbers
Problems:
  Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
  Two representations of 0 (±0):
1000
0000
Notes: Exercise

## Slide 40: Signed Binary Numbers
Two’s Complement Numbers
  Don’t have same problems as sign/magnitude numbers:
    Addition works
    Single representation for 0
  Msb has value of -2N-1
  Most positive 4-bit number:
  Most negative 4-bit number:
  The most significant bit still indicates the sign:
    1 = negative, 0 = positive
  Range of an N-bit two’s comp number:
Notes: Exercise

## Slide 41: Signed Binary Numbers
Two’s Complement Numbers
  Don’t have same problems as sign/magnitude numbers:
    Addition works
    Single representation for 0
  Msb has value of -2N-1
  Most positive 4-bit number: 0111
  Most negative 4-bit number: 1000
  The most significant bit still indicates the sign:
    1 = negative, 0 = positive
  Range of an N-bit two’s comp number: [-(2N-1), 2N-1-1]
Notes: Exercise

## Slide 42: Signed Binary Numbers
Two’s Complement Numbers
  “Taking the Two’s Complement
    Flip the sign of a two’s complement number
    Method:
    Invert the bits
    Add 1
Example 1: Flip the sign of 310 = 00112
Notes: Exercise

## Slide 43: Signed Binary Numbers
Two’s Complement Numbers
  “Taking the Two’s Complement
    Flip the sign of a two’s complement number
    Method:
    Invert the bits
    Add 1
Example 1: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
Notes: Exercise

## Slide 44: Signed Binary Numbers
Two’s Complement Numbers
Example 2: Take the two’s complement of 610 = 01102
Example 3: What is the decimal value of 10012?
Notes: Exercise

## Slide 45: Signed Binary Numbers
Two’s Complement Numbers
Example 2: Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
Example 3: What is the decimal value of 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Notes: Exercise

## Slide 46: Signed Binary Numbers
Two’s Complement Numbers
  Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Notes: Exercise

## Slide 47: Signed Binary Numbers
Two’s Complement Numbers
  Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Notes: Exercise

## Slide 48: Signed Binary Numbers
Two’s Complement Numbers
  Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Notes: Exercise

## Slide 49: Signed Binary Numbers
Two’s Complement Numbers
  Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Sign bit copied to msb’s
Number value is the same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Notes: Exercise

## Slide 50: Signed Binary Numbers
Two’s Complement Numbers
  Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 00112 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Notes: Exercise

## Slide 51: Number System Comparison
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Notes: Exercise