## Slide 1: Chapter 5 Digital Building Blocks (2) - Number Systems
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3: Number Systems
  Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
  Fractions
  Two common notations:
  Fixed-point: binary point fixed
  Floating-point: binary point floats to the right of the most significant 1

## Slide 4: Number Systems
  Fixed-Point Numbers
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
  Example:
    Represent 7.510 using 4 integer bits and 4 fraction bits ?
Notes: 0111 1000

## Slide 5: Number Systems
  Signed Fixed-Point Numbers
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  Two’s complement:
Notes: 0111 1000

## Slide 6: Number Systems
  Signed Fixed-Point numbers
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Notes: 0111 1000

## Slide 7: Number Systems
  Floating-Point Numbers
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
Example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Notes: 0111 1000

## Slide 8: Number Systems
  Floating-Point Numbers
Example: represent the value 22810 using a 32-bit floating point representation
Notes: three versions

## Slide 9: Number Systems
  Floating-Point Numbers: Representation 1:
Convert decimal to binary:
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Notes: three versions
(don’t reverse steps 1 & 2!):

## Slide 10: Number Systems
  Floating-Point Numbers: Representation 2:
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
No need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Notes: three versions

## Slide 11: Number Systems
  Floating-Point Numbers: Representation 3:
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Notes: three versions

## Slide 12: Number Systems
  Floating-Point Examples
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Notes: three versions

## Slide 13: Number Systems
  Floating-Point: Special Cases
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Notes: three versions

## Slide 14: Number Systems
  Floating-Point: Precisions
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Notes: three versions

## Slide 15: Number Systems
  Floating-Point: Rounding
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)
Notes: three versions

## Slide 16: Number Systems
  Floating-Point: Addition
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Notes: three versions

## Slide 17: Number Systems
  Floating-Point: Addition
Example: Add the following floating-point numbers:
0x3FC00000
0x40500000
Notes: three versions

## Slide 18: Number Systems
  Floating-Point: Addition
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Notes: three versions

## Slide 19: Number Systems
  Floating-Point: Addition
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Notes: three versions

## Slide 20: Number Systems
  Floating-Point: Addition
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Notes: three versions