## Slide 1: Chapter 5 Digital Building Blocks(1) -Arithmetic Circuits
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3: Introduction
  Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
  Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
  Will use these building blocks to build microprocessor

## Slide 4: 1-bit Adder

## Slide 5: 1-bit Adder

## Slide 6: 1-bit Adder

## Slide 7: Multi-bits Adder (CPAs)
  Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
  Carry-lookahead and prefix adders faster for large adders but require more hardware
Symbol

## Slide 8: Multi-bits Adder (CPAs)
  Ripple-Carry Adder :
  Chain 1-bit adders together
  Carry ripples through entire chain
  Disadvantage: slow
  Ripple-Carry Adder Delay: tripple = NtFA
where tFA is the delay of a full adder

## Slide 9: Multi-bits Adder (CPAs)
  Carry-Lookahead Adder
  Compute carry out (Cout) for k-bit blocks using generate and propagate signals
Definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Column i will generate a carry out if Ai AND Bi are both 1.
  Gi = Ai Bi
    Column i will propagate a carry in to the carry out if Ai OR Bi is 1.
  Pi = Ai + Bi
    The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1

## Slide 10: Multi-bits Adder (CPAs)
  Carry-Lookahead Adder
Procedure
  Step 1: Compute Gi and Pi for all columns
  Step 2: Compute G and P for k-bit blocks
  Step 3: Cin propagates through each k-bit propagate/generate block

## Slide 11: Multi-bits Adder (CPAs)
  Carry-Lookahead Adder
Example: 4-bit blocks (G3:0 and P3:0) :
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 ))
  P3:0 = P3P2 P1P0
Generally,
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj ))
  Pi:j = PiPi-1 Pi-2Pj
  Ci = Gi:j + Pi:j Ci-1

## Slide 12: Multi-bits Adder (CPAs)
  Carry-Lookahead Adder
32-bit CLA with
4-bit blocks

## Slide 13: Multi-bits Adder (CPAs)
  Carry-Lookahead Adder
CLA Delay
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR: delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16

## Slide 14: Multi-bits Adder (CPAs)
  Prefix Adder
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci-1
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages

## Slide 15: Multi-bits Adder (CPAs)
  Prefix Adder
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)

## Slide 16: Multi-bits Adder (CPAs)
  Prefix Adder
Generate and propagate signals for a block spanning bits i:j:
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if:
    both the upper and lower parts propagate the carry

## Slide 17: Multi-bits Adder (CPAs)
  Prefix Adder
Schematic

## Slide 18: Multi-bits Adder (CPAs)
  Prefix Adder
Delay
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)
  tXOR: delay to produce Si (XOR gate)

## Slide 19: Adder Delay Comparisons
  Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
  CLA has 4-bit blocks
  2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns

## Slide 20: Subtractor
Notes: 2’s complement – reverse each bits + 1: Cin is 1

## Slide 21: Comparator: Equality

## Slide 22: Comparator: Less than
Notes: negative number - sign bit is 1

## Slide 23: ALU: Arithmetic Logic Unit
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 24: ALU: Arithmetic Logic Unit
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT