## Slide 1: Chapter 6 Architecture (1)
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Goals
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lights, Camera, Action: Compiling, Assembling, & Loading
Odds and Ends

## Slide 3: Goals:
  Architecture
  programmer’s view of computer
  instructions & operand locations
  (Computer architecture does not define the underlying hardware implementation)
  Microarchitecture
  how to implement an architecture in hardware
Notes: Once you’ve learned one architecture, it’s easy to learn others

## Slide 4: Assembly Language
Instructions: commands in a computer’s language
  Assembly language
  human-readable format of instructions
  Machine language
  computer-readable format (1’s and 0’s)
MIPS architecture:
  Developed by John Hennessy and his colleagues at Stanford and in the 1980’s.
  Used in many commercial systems, including Silicon Graphics, Nintendo, and Cisco
Notes: Once you’ve learned one architecture, it’s easy to learn others

## Slide 5: Architecture Design Principles
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises

## Slide 6: MIPS instruction: Addition
Instruction: Addition
C Code
a = b + c;
MIPS assembly code
add a, b, c
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is performed)
a: destination operand (to which the result is written)

## Slide 7: MIPS instruction: Subtraction
Instruction: Subtraction
C Code
a = b - c;
MIPS assembly code
sub a, b, c
sub: mnemonic
b, c: source operands
a: destination operand

## Slide 8: Architecture Design Principles
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
Easier to encode and handle in hardware
  Make the common case fast
  Smaller is faster
  Good design demands good compromises
Notes: More complex high-level code translates into multiple instructions, like MIPS

## Slide 9: Architecture Design Principles
Simplicity favors regularity
  More complex code is handled by multiple MIPS instructions.
C Code
a = b + c - d;
MIPS assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d

## Slide 10: Architecture Design Principles
Simplicity favors regularity
  Make the common case fast
Only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
  MIPS is a reduced instruction set computer (RISC), with a small number of simple instructions
  Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
  Smaller is faster
  Good design demands good compromises

## Slide 11: Operands
Operand location: physical location in computer
  Registers
Registers are faster than memory
MIPS has 32 32-bit registers
“32-bit architecture” -- 32-bit data
  Memory
  Constants (also called immediates)

## Slide 12: Architecture Design Principles
Simplicity favors regularity
  Make the common case fast
  Smaller is faster
  MIPS includes only a small number of registers
  Good design demands good compromises

## Slide 13: MIPS Register Set
Name | Register Number | Usage
$0 | 0 | the constant value 0
$at | 1 | assembler temporary
$v0-$v1 | 2-3 | Function return values
$a0-$a3 | 4-7 | Function arguments
$t0-$t7 | 8-15 | temporaries
$s0-$s7 | 16-23 | saved variables
$t8-$t9 | 24-25 | more temporaries
$k0-$k1 | 26-27 | OS temporaries
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | Function return address

## Slide 14: MIPS Operands: Registers
Registers:
  $ before name & number
  Example: $0, “register zero”, “dollar zero”
Registers used for specific purposes:
  $0 always holds the constant value 0.
  the saved registers, $s0-$s7, used to hold variables
  the temporary registers, $t0 - $t9, used to hold intermediate values during a larger computation
  No direct access to some registers:
  Program Counter (PC): Store the address of the instruction executing;
  "hi" and "lo" registers: used in multiplication and division;
Notes: Programmers change the “PC” on branches and jumps
multiplication may result in a 64-bit product and division results in a quotient and remainder
There are special instructions to move data to and from the “hi” and “lo” registers

## Slide 15: MIPS Operands: Registers
Registers:
  add instruction
C Code
a = b + c;
MIPS assembly code
add a, b, c
# $s0 = a, $s1 = b, $s2 = c
add $s0, $s1, $s2

## Slide 16: MIPS Operands: Memory
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers

## Slide 17: Word-Addressable Memory
Each 32-bit data word has a unique address

## Slide 18: Word-Addressable Memory
Reading word-addressable memory
Memory read called load
Mnemonic: load word (lw)
Format: lw $s0, 5($t1)
Address calculation:
  add base address ($t1) to the offset (5)
  address = ($t1 + 5)
Result:
  $s0 holds the value at address ($t1 + 5)
Notes: Any register may be used as base address

## Slide 19: Word-Addressable Memory
Reading word-addressable memory
Example: read a word of data at memory address 1 into $s3
  address = ($0 + 1) = 1
  $s3 = 0xF2F1AC07
Assembly code
lw $s3, 1($0) # read memory word 1 into $s3

## Slide 20: Word-Addressable Memory
Writing word-addressable memory
Memory read called store
Mnemonic: store word (sw)
Example: Write (store) the value in $t4 into memory address 3
  add the base address ($0) to the offset (0x3)
  address: ($0 + 0x3) = 3
  Offset can be written in decimal
  (default) or hexadecimal
Assembly code
sw $t4, 0x3 ($0) # write value in $t4
# to memory word 3

## Slide 21: Byte-Addressable Memory
Each data byte has unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4

## Slide 22: Byte-Addressable Memory
Reading byte-addressable memory
Example: Load a word of data at memory address 4 into $s3. $s3 holds the value 0xF2F1AC07 after load
MIPS assembly code
lw $s3, 4($0) # read word at
# address 4 into $s3

## Slide 23: Byte-Addressable Memory
Writing byte-addressable memory
Example: stores the value held in $t7 into memory address 0x2C (44)
MIPS assembly code
sw $t7, 44($0) # write $t7 into address 44

## Slide 24: Big-Endian & Little Endian
How to number bytes within a word?
Little-endian: byte numbers start at the little (least significant) end
Big-endian: byte numbers start at the big (most significant) end
Word address is the same for big- or little-endian

## Slide 25: Big-Endian & Little Endian
Example:
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)

## Slide 26: Big-Endian & Little Endian
Example:
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)
Big-endian:
0x00000045
Little-endian:
0x00000067

## Slide 27: Architecture Design Principles
Simplicity favors regularity
  Make the common case fast
  Smaller is faster
  Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).

## Slide 28: MIPS Operands: Constants/Immediates
lw and sw use constants or immediates
immediately available from instruction
16-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?

## Slide 29: Machine Language
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  R-Type: register operands
  I-Type: immediate operand
  J-Type: for jumping

## Slide 30: R-Type Instructions
Register-type
3 register operands:
  rs, rt: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode (0 for R-type instructions)
  funct: the function
  with opcode, tells computer what operation to perform
  shamt: the shift amount for shift instructions, otherwise it’s 0

## Slide 31: R-Type Examples
Note the order of registers in the assembly code:
add rd, rs, rt
Notes: All R-type instructions have an opcode “0”.

## Slide 32: I-Type Instructions
Immediate-type
3 operands:
  rs, rt: register operands
  imm: 16-bit two’s complement immediate
Other fields:
  op: the opcode
  Simplicity favors regularity: all instructions have opcode
  Operation is completely determined by opcode

## Slide 33: I-Type Examples
Note the differing order of registers in assembly and machine codes:
addi rt, rs, imm
lw rt, imm(rs)
sw rt, imm(rs)
Notes: addi: rt is the destination

## Slide 34: J-Type Instructions
Jump-type
26-bit address operand (addr)
Used for jump instructions (j)

## Slide 35: Review: Instruction format

## Slide 36: Power of the Stored Program
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation

## Slide 37: The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 38: Interpreting Machine Code
Start with opcode: tells how to parse rest
If opcode all 0’s
  R-type instruction
  Function bits tell operation
Otherwise
  opcode tells operation