## Slide 1: Chapter 6 Architecture (3)
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Goals
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lights, Camera, Action: Compiling, Assembling, & Loading
Odds and Ends

## Slide 3: Programming
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Common high-level software constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 4: Arrays
Array Example
5-element array
Base address = 0x12348000 (address of first element, array[0])
First step in accessing an array: load base address into a register

## Slide 5: Arrays
Accessing Arrays
// C Code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# MIPS assembly code
# array base address = $s0
lui $s0, 0x1234 # 0x1234 in upper half of $S0
ori $s0, $s0, 0x8000 # 0x8000 in lower half of $s0
lw $t1, 0($s0) # $t1 = array[0]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 0($s0) # array[0] = $t1
lw $t1, 4($s0) # $t1 = array[1]
sll $t1, $t1, 1 # $t1 = $t1 * 2
sw $t1, 4($s0) # array[1] = $t1

## Slide 6: Arrays
Arrays using For-Loops
// C Code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# MIPS assembly code
# $s0 = array base address, $s1 = i

## Slide 7: Arrays
Arrays using For-Loops
# MIPS assembly code
# $s0 = array base address, $s1 = i
# initialization code
lui $s0, 0x23B8 # $s0 = 0x23B80000
ori $s0, $s0, 0xF000 # $s0 = 0x23B8F000
addi $s1, $0, 0 # i = 0
addi $t2, $0, 1000 # $t2 = 1000
loop:
slt $t0, $s1, $t2 # i < 1000?
beq $t0, $0, done # if not then done
sll $t0, $s1, 2 # $t0 = i * 4 (byte offset)
add $t0, $t0, $s0 # address of array[i]
lw $t1, 0($t0) # $t1 = array[i]
sll $t1, $t1, 3 # $t1 = array[i] * 8
sw $t1, 0($t0) # array[i] = array[i] * 8
addi $s1, $s1, 1 # i = i + 1
j loop # repeat
done:

## Slide 8: Function calls
Caller: calling function (“main()”)
Callee: called function (“sum()”)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}

## Slide 9: Function calls
Function Conventions
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller

## Slide 10: Function calls
MIPS Function Conventions
Call Function: jump and link (jal)
Return from function: jump register (jr)
Arguments: $a0 - $a3
Return value: $v0

## Slide 11: Function calls
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
MIPS assembly code
0x00400200 main: jal simple
0x00400204 add $s0, $s1, $s2
...
0x00401020 simple: jr $ra
jal: jumps to simple
$ra = PC + 4 = 0x00400204
jr $ra: jumps to address in $ra (0x00400204)

## Slide 12: Function calls
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
MIPS conventions:
Argument values: $a0 - $a3
Return value: $v0

## Slide 13: Function calls
MIPS assembly code
# $s0 = y
main:
...
addi $a0, $0, 2 # argument 0 = 2
addi $a1, $0, 3 # argument 1 = 3
addi $a2, $0, 4 # argument 2 = 4
addi $a3, $0, 5 # argument 3 = 5
jal diffofsums # call Function
add $s0, $v0, $0 # y = returned value
...
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller

## Slide 14: Function calls
MIPS assembly code
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller
diffofsums overwrote 3 registers: $t0, $t1, $s0
diffofsums can use stack to temporarily store registers

## Slide 15: Function calls
Stack
Memory used to temporarily save variables
Last-In-First-Out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space is no longer needed

## Slide 16: Function calls
Stack
Grows down (from higher to lower memory addresses)
Stack pointer: $sp points to top of the stack

## Slide 17: Function calls
Stack
Called functions must have no unintended side effects
diffofsums overwrites 3 registers: $t0, $t1, $s0
# MIPS assembly
# $s0 = result
diffofsums:
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
jr $ra # return to caller

## Slide 18: Function calls
Stack
Called functions must have no unintended side effects
diffofsums overwrites 3 registers: $t0, $t1, $s0
Storing register values on Stack

## Slide 19: Function calls
Stack
Called functions must have no unintended side effects
# $s0 = result
diffofsums:
addi $sp, $sp, -12 # make space on stack
# to store 3 registers
sw $s0, 8($sp) # save $s0 on stack
sw $t0, 4($sp) # save $t0 on stack
sw $t1, 0($sp) # save $t1 on stack
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $t1, 0($sp) # restore $t1 from stack
lw $t0, 4($sp) # restore $t0 from stack
lw $s0, 8($sp) # restore $s0 from stack
addi $sp, $sp, 12 # deallocate stack space
jr $ra # return to caller

## Slide 20: Function calls
Stack
Registers
Preserved Callee-Saved | Nonpreserved Caller-Saved
$s0-$s7 | $t0-$t9
$ra | $a0-$a3
$sp | $v0-$v1
stack above $sp | stack below $sp

## Slide 21: Function calls
Multiple Function Calls
proc1:
addi $sp, $sp, -4 # make space on stack
sw $ra, 0($sp) # save $ra on stack
jal proc2
...
lw $ra, 0($sp) # restore $s0 from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller

## Slide 22: Function calls
Stack
Storing saved registers on stack
# $s0 = result
diffofsums:
addi $sp, $sp, -4 # make space on stack to
# store one register
sw $s0, 0($sp) # save $s0 on stack
# no need to save $t0 or $t1
add $t0, $a0, $a1 # $t0 = f + g
add $t1, $a2, $a3 # $t1 = h + i
sub $s0, $t0, $t1 # result = (f + g) - (h + i)
add $v0, $s0, $0 # put return value in $v0
lw $s0, 0($sp) # restore $s0 from stack
addi $sp, $sp, 4 # deallocate stack space
jr $ra # return to caller

## Slide 23: Function calls
Recursive function calls
High-level code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}

## Slide 24: Function calls
Recursive function calls
MIPS assembly code
0x90 factorial: addi $sp, $sp, -8 # make room
0x94 sw $a0, 4($sp) # store $a0
0x98 sw $ra, 0($sp) # store $ra
0x9C addi $t0, $0, 2
0xA0 slt $t0, $a0, $t0 # a <= 1 ?
0xA4 beq $t0, $0, else # no: go to else
0xA8 addi $v0, $0, 1 # yes: return 1
0xAC addi $sp, $sp, 8 # restore $sp
0xB0 jr $ra # return
0xB4 else: addi $a0, $a0, -1 # n = n - 1
0xB8 jal factorial # recursive call
0xBC lw $ra, 0($sp) # restore $ra
0xC0 lw $a0, 4($sp) # restore $a0
0xC4 addi $sp, $sp, 8 # restore $sp
0xC8 mul $v0, $a0, $v0 # n * factorial(n-1)
0xCC jr $ra # return

## Slide 25: Function calls
Recursive function calls

## Slide 26: Function calls
Summery
Caller
  Put arguments in $a0-$a3
  Save any needed registers ($ra, maybe $t0-t9)
  jal callee
  Restore registers
  Look for result in $v0
Callee
  Save registers that might be disturbed ($s0-$s7)
  Perform function
  Put result in $v0
  Restore registers
  jr $ra