## Slide 1: Chapter 7 Mircoarchitecture (1)
Suffolk County Community College
CSE 222, Spring 2020

## Slide 2: Topics:
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3: Introduction
  Microarchitecture
  How to implement an architecture in hardware
  Processor:
  Datapath: functional blocks
  Control: control signals

## Slide 4: Microarchitecture
Multiple implementations for a single architecture:
  Single-cycle:
  Each instruction executes in a single cycle
  Multicycle:
  Each instruction is broken into series of shorter steps
  Pipelined:
  Each instruction broken up into series of steps & multiple instructions execute at once

## Slide 5: Processor Performance
Program execution time :
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance

## Slide 6: MIPS Processor
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq

## Slide 7: Architectural State
Determines everything about a processor:
  PC
  32 registers
  Memory
  Turing Machine
  https://www.cl.cam.ac.uk/projects/raspberrypi/tutorials/turing-machine/one.html

## Slide 8: MIPS State Elements

## Slide 9: Single–Cycle MIPS Processor
Datapath
Operates on words of data
Contains structures of memories, registers, ALUs, multiplexer
Control
Control unit produces multiplexer select, register enable, memory write signals to control the operation of datapath
Notes: Once you’ve learned one architecture, it’s easy to learn others

## Slide 10: Single–Cycle Datapath: lw: fetch
STEP 1: Fetch instruction
Notes: MIPS instruction: lw $rs, $rt, imm
Machine code: lw $rt, offset($rs)
imm = offset

## Slide 11: Single–Cycle Datapath: lw: Register Read
STEP 2: Read source operands from RF

## Slide 12: Single–Cycle Datapath: lw: Immediate
STEP 3: Sign-extend the immediate

## Slide 13: Single–Cycle Datapath: lw: Address
STEP 4: Compute the memory address

## Slide 14: Single–Cycle Datapath: lw: Memory Read
STEP 5: Read data from memory and write it back to register file

## Slide 15: Single–Cycle Datapath: lw: PC Increment
STEP 6: Determine address of next instruction

## Slide 16: Single–Cycle Datapath: sw
SW: Write data in rt to memory

## Slide 17: Single–Cycle Datapath: R-type
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)

## Slide 18: Single–Cycle Datapath: beq
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)

## Slide 19: Single–Cycle Processor
Notes: Once you’ve learned one architecture, it’s easy to learn others

## Slide 20: Single–Cycle Control

## Slide 21: Review: ALU
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 22: Control Unit: ALU Decoder
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)

## Slide 23: Control Unit Main Decoder
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Notes: Once you’ve learned one architecture, it’s easy to learn others

## Slide 24: Control Unit Main Decoder
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01

## Slide 25: Single-Cycle Datapath: or

## Slide 26: Extended Functionality: addi

## Slide 27: Control Unit: addi
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 

## Slide 28: Control Unit: addi
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00

## Slide 29: Extended Functionality: j

## Slide 30: Control Unit: j
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 

## Slide 31: Control Unit: j
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1

## Slide 32: Processor Performance
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC

## Slide 33: Single-Cycle Performance
TC limited by critical path (lw)

## Slide 34: Single-Cycle Performance
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup

## Slide 35: Single-Cycle Performance
Example:
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?

## Slide 36: Single-Cycle Performance
Example:
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps

## Slide 37: Single-Cycle Performance
Example:
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(925 × 10-12 s)
= 92.5 seconds